## Slide 1: Pipeline Hazards
Textbook Chapter 4 – The Processor
Lecture 26

## Slide 2: Data Hazard – Example 4
Make pipeline diagram for the code segment given below, and identify data hazards
lw $s0, 20($t1)
sub $t2, $s0, $t3

## Slide 3: Data Hazard – Example 4 (contd.)
Make pipeline diagram for the code segment given below, and identify data hazards
Solution:
lw $s0, 20($t1)
sub $t2, $s0, $t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $s0, 20($t1) | IF | ID | EX | MEM | WB |  | 
sub $t2, $s0, $t3 |  | IF | ID | EX | MEM | WB | 

## Slide 4: Data Hazard – Example 4 (contd.)
Make pipeline diagram for the code segment given below, and identify data hazards
Solution:
lw $s0, 20($t1)
sub $t2, $s0, $t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $s0, 20($t1) | IF | ID | EX | MEM | WB |  | 
sub $t2, $s0, $t3 |  | IF | ID | EX | MEM | WB | 
Find Dependences
Is Forwarding possible?

## Slide 5: Data Hazard – Example 4 (contd.)
Make pipeline diagram for the code segment given below, and identify data hazards
Solution:
lw $s0, 20($t1)
sub $t2, $s0, $t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $s0, 20($t1) | IF | ID | EX | MEM | WB |  | 
sub $t2, $s0, $t3 |  | IF | ID | EX | MEM | WB | 
Find Dependences
Solution: Stall the pipeline

## Slide 6: Data Hazard – Example 4 (contd.)
Make pipeline diagram for the code segment given below, and identify data hazards
Solution:
lw $s0, 20($t1)
sub $t2, $s0, $t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $s0, 20($t1) | IF | ID | EX | MEM | WB |  | 
sub $t2, $s0, $t3 |  | IF | ID |  | EX | MEM | WB
Find Dependences
Solution: Stall the pipeline

## Slide 7: Data Hazard – Example 4 (contd.)
Make pipeline diagram for the code segment given below, and identify data hazards
Solution:
lw $s0, 20($t1)
sub $t2, $s0, $t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $s0, 20($t1) | IF | ID | EX | MEM | WB |  | 
sub $t2, $s0, $t3 |  | IF | ID | Stall | Stall | Stall | 
sub $t2, $s0, $t3 |  |  |  |  | EX | MEM | WB
Find Dependences
Solution: Stall the pipeline

## Slide 8: Data Hazard – Example 4 (contd.)
Make pipeline diagram for the code segment given below, and identify data hazards
Solution:
lw $s0, 20($t1)
sub $t2, $s0, $t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $s0, 20($t1) | IF | ID | EX | MEM | WB |  | 
sub $t2, $s0, $t3 |  | IF | ID | Stall | Stall | Stall | 
sub $t2, $s0, $t3 |  | IF | ID | ID | EX | MEM | WB
Find Dependences
Solution: Stall the pipeline

## Slide 9: Data Hazard – Example 4 (contd.)
Make pipeline diagram for the code segment given below, and identify data hazards
Solution:
lw $s0, 20($t1)
sub $t2, $s0, $t3
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $s0, 20($t1) | IF | ID | EX | MEM | WB |  | 
 |  | Stall | Stall | Stall | Stall | Stall | 
sub $t2, $s0, $t3 |  |  | IF | ID | EX | MEM | WB
Find Dependences
Solution: Stall the pipeline

## Slide 10: Data Hazard – Example 4 Pipeline Stall (Bubble)
we cannot know until after the subtract instruction is fetched and decoded whether or not a stall will be necessary
CC1
CC2
CC3
CC4
CC5
CC6
CC7
Notes: FIGURE 4.30 We need a stall even with forwarding when an R-format instruction following a load tries to use the data. Without the stall, the path from memory access stage output to execution stage input would be going backward in time, which is impossible. Th is fi gure is actually a simplifi cation, since we cannot know until aft er the subtract instruction is fetched and decoded whether or not a stall will be necessary. Section 4.7 shows the details of what really happens in the case of a hazard.

## Slide 11: Data Hazard – Example 5
Make pipeline diagram for the code segment given below, and identify data dependences and hazards.
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7

## Slide 12: Data Hazard – Example 5
Make pipeline diagram for the code segment given below, and identify data dependences and hazards.
Solution:
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
Check and fix (if required) the $4 dependency yourself.

## Slide 13: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 |  |  |  |  |  | 
lw $2, 20($1) | IF |  |  |  |  |  | 

## Slide 14: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 |  |  |  |  | 
lw $2, 20($1) | IF | ID |  |  |  |  | 
and $4, $2, $5 |  | IF |  |  |  |  | 

## Slide 15: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 |  |  |  | 
lw $2, 20($1) | IF | ID | EX |  |  |  | 
and $4, $2, $5 |  | IF | ID |  |  |  | 
or $8, $2, $6 |  |  | IF |  |  |  | 
Assume there is no dependency, how will pipelining work?

## Slide 16: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $2, 20($1) | IF | ID | EX | MEM | WB |  | 
and $4, $2, $5 |  | IF | ID | EX | MEM | WB | 
or $8, $2, $6 |  |  | IF | ID | EX | MEM | WB
Assume there is no dependency, how will pipelining work?

## Slide 17: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  |  | 
and $4, $2, $5 |  | IF | ID | EX | MEM | WB |  |  | 
or $8, $2, $6 |  |  | IF | ID | EX | MEM | WB |  | 
add $9, $4, $2 |  |  |  | IF | ID | EX | MEM | WB | 
slt $1, $6, $7 |  |  |  |  | IF | ID | EX | MEM | WB
Assume there is no dependency, how will pipelining work?

## Slide 18: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 |  |  |  | 
lw $2, 20($1) | IF | ID | EX |  |  |  | 
and $4, $2, $5 |  | IF | ID |  |  |  | 
or $8, $2, $6 |  |  | IF |  |  |  | 
At ID of “and $4, $2, $5”, we get to know that we have to stall its EX
“or $8, $2, $6 ” is already in pipeline, this should not be missed

## Slide 19: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 |  | 
lw $2, 20($1) | IF | ID | EX | MEM | WB |  | 
and $4, $2, $5 |  | IF | ID |  | EX |  | 
or $8, $2, $6 |  |  | IF |  |  |  | 
At ID of “and $4, $2, $5”, we get to know that we have to stall its EX
“or $8, $2, $6 ” is already in pipeline, this should not be missed
At CC5, we can execute “and $4, $2, $5” having Mem content forwarded from Mem/WB Register

## Slide 20: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $2, 20($1) | IF | ID | EX | MEM | WB |  | 
and $4, $2, $5 |  | IF | ID |  | EX | MEM | WB
or $8, $2, $6 |  |  | IF |  |  |  | 
At ID of “and $4, $2, $5”, we get to know that we have to stall its EX
“or $8, $2, $6 ” is already in pipeline, this should not be missed
At CC5, we can execute “and $4, $2, $5” having Mem content forwarded from Mem/WB Register

## Slide 21: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7
lw $2, 20($1) | IF | ID | EX | MEM | WB |  | 
and $4, $2, $5 |  | IF | ID |  | EX | MEM | WB
or $8, $2, $6 |  |  | IF |  |  |  | 
At ID of “and $4, $2, $5”, we get to know that we have to stall its EX
“or $8, $2, $6 ” is already in pipeline, this should not be missed
At CC5, we can execute “and $4, $2, $5” having Mem content forwarded from Mem/WB Register
We need to stop “or $8, $2, $6 ” at IF at CC4

## Slide 22: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | 
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  | 
and $4, $2, $5 |  | IF | ID |  | EX | MEM | WB | 
or $8, $2, $6 |  |  | IF |  | ID | EX | MEM | WB
At ID of “and $4, $2, $5”, we get to know that we have to stall its EX
“or $8, $2, $6 ” is already in pipeline, this should not be missed
At CC5, we can execute “and $4, $2, $5” having Mem content forwarded from Mem/WB Register
We need to stop “or $8, $2, $6 ” at IF at CC4

## Slide 23: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | 
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  | 
and $4, $2, $5 |  | IF | ID | ID | EX | MEM | WB | 
or $8, $2, $6 |  |  | IF | IF | ID | EX | MEM | WB
In CC3 we have to do following
  Keep and in ID at CC4
  Keep or in IF at CC4

## Slide 24: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  |  |  | 
and $4, $2, $5 |  | IF | ID | ID | EX | MEM | WB |  |  | 
or $8, $2, $6 |  |  | IF | IF | ID | EX | MEM | WB |  | 
add $9, $4, $2 |  |  |  |  | IF | ID | EX | MEM | WB | 
slt $1, $6, $7 |  |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 25: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  |  |  | 
and $4, $2, $5 |  | IF | ID | ID | EX | MEM | WB |  |  | 
or $8, $2, $6 |  |  | IF | IF | ID | EX | MEM | WB |  | 
add $9, $4, $2 |  |  |  |  | IF | ID | EX | MEM | WB | 
slt $1, $6, $7 |  |  |  |  |  | IF | ID | EX | MEM | WB
Requirements:
1- We need to stop PC from changing. Don’t let “add $9, $4, $2” in.
2- Hold “IF/ID” Pipeline register to keep “or $8, $2, $6 ”
3- Hold “ID/EX” to execute “and $4, $2, $5”

## Slide 26
Stall
Implementation
Notes: FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplifi ed—the sign-extended immediate and branch logic are missing— this drawing gives the essence of the forwarding hardware requirements.

## Slide 27
Stall
Implementation
ID.rs
ID.rt
EX.rt
Notes: FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplifi ed—the sign-extended immediate and branch logic are missing— this drawing gives the essence of the forwarding hardware requirements.

## Slide 28
Stall
Implementation
ID.rs
ID.rt
EX.rt
Notes: FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplified—the sign-extended immediate and branch logic are missing— this drawing gives the essence of the forwarding hardware requirements.

## Slide 29: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  |  |  | 
and $4, $2, $5 |  | IF | ID | ID | EX | MEM | WB |  |  | 
or $8, $2, $6 |  |  | IF | IF | ID | EX | MEM | WB |  | 
add $9, $4, $2 |  |  |  |  | IF | ID | EX | MEM | WB | 
slt $1, $6, $7 |  |  |  |  |  | IF | ID | EX | MEM | WB
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  |  |  | 
and $4, $2, $5 (become NOP) |  | IF | ID | STAL in EX | STALL in Mem | STALL in WB |  |  |  | 
and $4, $2, $5 |  |  |  | ID | EX | MEM | WB |  |  | 
or $8, $2, $6 |  |  | IF | IF | ID | EX | MEM | WB |  | 
add $9, $4, $2 |  |  |  |  | IF | ID | EX | MEM | WB | 
slt $1, $6, $7 |  |  |  |  |  | IF | ID | EX | MEM | WB
Stall = Bubble
Another
Way
To show the
Same
Execution

## Slide 30: Data Hazard – Example 5 (contd.)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $6
add $9, $4, $2
slt $1, $6, $7
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  |  |  | 
and $4, $2, $5 |  | IF | ID | ID | EX | MEM | WB |  |  | 
or $8, $2, $6 |  |  | IF | IF | ID | EX | MEM | WB |  | 
add $9, $4, $2 |  |  |  |  | IF | ID | EX | MEM | WB | 
slt $1, $6, $7 |  |  |  |  |  | IF | ID | EX | MEM | WB
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9 | CC10
lw $2, 20($1) | IF | ID | EX | MEM | WB |  |  |  |  | 
nop |  | STALL | STALL | STALL | STALL | STALL |  |  |  | 
and $4, $2, $5 |  |  | IF | ID | EX | MEM | WB |  |  | 
or $8, $2, $6 |  |  |  | IF | ID | EX | MEM | WB |  | 
add $9, $4, $2 |  |  |  |  | IF | ID | EX | MEM | WB | 
slt $1, $6, $7 |  |  |  |  |  | IF | ID | EX | MEM | WB
Another
Way
To show the
Same
Sequence

## Slide 31: Hazard Detection Unit
Operates during the ID stage so that it can insert the stall between the load and its use
Hazard Detection Control
Preventing the PC register and the IF/ID pipeline register from changing
The instruction in the IF stage will continue to be read using the same PC
The registers in the ID stage will continue to be read using the same instruction fields in the IF/ID pipeline register
Setting all nine control signals in the EX, MEM, and WB stages will create a “do nothing” or nop instruction
No registers or memories are written if the control values are all 0
Hazard Detection Control

## Slide 32: Data Hazards – Example 5 Pipeline Diagram

## Slide 33: Data Hazards – Example 5 Pipeline Diagram

## Slide 34: Data Hazards – Example 5 Solution Stall
Nop: An instruction that does no operation to change state
Notes: FIGURE 4.59 The way stalls are really inserted into the pipeline. A bubble is inserted beginning in clock cycle 4, by changing the and instruction to a nop. Note that the and instruction is really fetched and decoded in clock cycles 2 and 3, but its EX stage is delayed until clock cycle 5 (versus the unstalled position in clock cycle 4). Likewise the OR instruction is fetched in clock cycle 3, but its ID stage is delayed until clock cycle 5 (versus the unstalled clock cycle 4 position). Aft er insertion of the bubble, all the dependences go forward in time and no further hazards occur

## Slide 35: Data Hazard – Practice Problems
Make pipeline diagram for the code segment given below, and identify data dependences and hazards.
(a)
lw $2, 20($1)
and $4, $2, $5
or $8, $2, $4
add $9, $4, $2
slt $1, $6, $7
(b)
lw $2, 20($1)
add $3, $4,$5
and $4, $2, $5
or $8, $2, $4
add $9, $4, $2
slt $1, $6, $7

## Slide 36: Pipeline Stall
Pipeline Stall (Bubble): A stall initiated in order to resolve a hazard.
Load-use data hazard: A specific form of data hazard in which the data being loaded by a load instruction has not yet become available when it is needed by another instruction.
Bubbling the pipeline, also termed a pipeline break or pipeline stall, is a method to preclude data, structural, and branch hazards. As instructions are fetched, control logic determines whether a hazard could/will occur. If this is true, then the control logic inserts no operations (NOPs) into the pipeline. Thus, before the next instruction (which would cause the hazard) executes, the prior one will have had sufficient time to finish and prevent the hazard. If the number of NOPs equals the number of stages in the pipeline, the processor has been cleared of all instructions and can proceed free from hazards. All forms of stalling introduce a delay before the processor can resume execution.

## Slide 37: Example 6 -Reordering Code to Avoid Pipeline Stalls
Consider the following code segment in C:
a = b + e;
c = b + f;
Here is the generated MIPS code for this segment, assuming all variables are in
memory and are addressable as off sets from $t0:
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1,$t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1,$t4
sw $t5, 16($t0)
Find the hazards in the preceding code segment and reorder the instructions to avoid any pipeline stalls
Practice Question: Make Pipeline Execution for following code, properly show hazards fixes.

## Slide 38: Example 6 -Reordering Code to Avoid Pipeline Stalls (Contd.)
Solution:
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1,$t2
sw $t3, 12($t0)
add $t5, $t1,$t4
sw $t5, 16($t0)
On a pipelined processor with forwarding, the reordered sequence will complete in two fewer cycles than the original version.
Practice Question: Make Pipeline Execution for following code, properly show hazards fixes.

## Slide 39: Branch Instruction Operation on Datapath

## Slide 40: Branch Instruction Operation on Datapath
1
2
3
4
5
0

## Slide 41: Branch Instruction Operation on Pipelined Datapath
Notes: FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplifi ed—the sign-extended immediate and branch logic are missing— this drawing gives the essence of the forwarding hardware requirements.

## Slide 42: Branch Instruction Operation on Pipelined Datapath
1
2
3
5
4
Notes: FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplifi ed—the sign-extended immediate and branch logic are missing— this drawing gives the essence of the forwarding hardware requirements.

## Slide 43: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)

## Slide 44: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 |  |  |  |  |  | 
sub $10, $4, $8 | IF |  |  |  |  |  | 

## Slide 45: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 | CC2 |  |  |  |  | 
sub $10, $4, $8 | IF | ID |  |  |  |  | 
beq $1, $3, 7 |  | IF |  |  |  |  | 

## Slide 46: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 | CC2 | CC3 |  |  |  | 
sub $10, $4, $8 | IF | ID | EX |  |  |  | 
beq $1, $3, 7 |  | IF | ID |  |  |  | 
??? |  |  | IF? |  |  |  | 

## Slide 47: Branch Prediction
How to handle Branches? Solution: Branch Prediction
Branch Prediction Strategies:
Always Untaken i.e. fetch instruction at PC + 4
Always Taken i.e. PC = PC + 4 + Offset
Delayed Branch i.e. add some code between branch instruction and target instruction
Some branches always taken and some branches always not taken e.g. at the bottom of loops are branches that jump back to the top of the loop
Dynamic Prediction on the basis of history of a branch
When the guess is wrong, the pipeline control must ensure that the instructions following the wrongly guessed branch have no effect and must restart the pipeline from the proper branch address.

## Slide 48: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 | CC2 | CC3 |  |  |  | 
sub $10, $4, $8 | IF | ID | EX |  |  |  | 
beq $1, $3, 7 |  | IF | ID |  |  |  | 
and $12, $2, $5 |  |  | IF |  |  |  | 

## Slide 49: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 | CC2 | CC3 | CC4 |  |  | 
sub $10, $4, $8 | IF | ID | EX | MEM |  |  | 
beq $1, $3, 7 |  | IF | ID | EX |  |  | 
and $12, $2, $5 |  |  | IF | ID |  |  | 
or $13, $2, $6 |  |  |  | IF |  |  | 
Have you noticed any problem?
Is our prediction Correct?
When will we get to know if the prediction was correct or not?

## Slide 50: Branch Instruction Operation on Pipelined Datapath
1
2
3
5
4
t4
t5
t6
CC3
CC5
CC4
CC4
Notes: FIGURE 4.60 Pipelined control overview, showing the two multiplexors for forwarding, the hazard detection unit, and the forwarding unit. Although the ID and EX stages have been simplifi ed—the sign-extended immediate and branch logic are missing— this drawing gives the essence of the forwarding hardware requirements.

## Slide 51: Example 7 – Strategy: Always NOT Taken
Flush: To discard instructions in a pipeline, usually due to an unexpected event
CC1
CC2
CC3
CC4
CC5
CC6
CC7

## Slide 52: Branch with Datapath Optimization
Flush: To discard instructions in a pipeline, usually due to an unexpected event
Branch
Branch

## Slide 53
Flush: To discard instructions in a pipeline, usually due to an unexpected event
$0, $0, 0
Branch with Datapath Optimization

## Slide 54: Pipelined Datapath

## Slide 55: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 | CC2 | CC3 | CC4 |  |  | 
sub $10, $4, $8 | IF | ID | EX | MEM |  |  | 
beq $1, $3, 7 |  | IF | ID | EX |  |  | 
and $12, $2, $5 |  |  | IF | Bubble |  |  | 
lw $4, 50($7) |  |  |  | IF |  |  | 

## Slide 56: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 | CC2 | CC3 | CC4 | CC5 |  | 
sub $10, $4, $8 | IF | ID | EX | MEM | WB |  | 
beq $1, $3, 7 |  | IF | ID | EX | MEM |  | 
and $12, $2, $5 |  |  | IF | Bubble | Bubble |  | 
lw $4, 50($7) |  |  |  | IF | ID |  | 
Next Instruction |  |  |  |  | IF |  | 

## Slide 57: Example 7 – Pipeline Branch
Draw pipeline diagram for the code segment given below:
36 sub $10, $4, $8
40 beq $1, $3, 7 # PC-relative branch to 40 + 4 + 7 * 4 = 72
44 and $12, $2, $5
48 or $13, $2, $6
52 add $14, $4, $2
56 slt $15, $6, $7
. . .
72 lw $4, 50($7)
 | CC1 | CC2 | CC3 | CC4 | CC5 | CC6 | CC7 | CC8 | CC9
sub $10, $4, $8 | IF | ID | EX | MEM | WB |  |  |  | 
beq $1, $3, 7 |  | IF | ID | EX | MEM | WB |  |  | 
and $12, $2, $5 |  |  | IF | Bubble | Bubble | Bubble | Bubble |  | 
lw $4, 50($7) |  |  |  | IF | ID | EX | MEM | WB | 
Next Instruction |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 58: Control Hazards (Branch Hazards)
Hazard arising from the need to make a decision based on the results of one instruction while others are executing.
Control hazard occurs when the pipeline makes wrong decisions on branch prediction and therefore brings instructions into the pipeline that must subsequently be discarded.
The term branch hazard also refers to a control hazard.
We must begin fetching the instruction following the branch on the very next clock cycle. Nevertheless, the pipeline cannot possibly know what the next instruction should be, since it only just received the branch instruction from memory!

## Slide 59: Summary – Pipeline Hazards
Three type of Pipeline Hazards
Structural Hazard
  Add Resource
  Stall
Data Hazard
  Forwarding
  Stall the Pipeline
Control Hazard
  Stall

## Slide 60: Reference
David A. Patterson, John L. Hennessy, Computer Organization and Design: The hardware/software interface – Chapter 4.
https://en.wikipedia.org/wiki/Hazard_(computer_architecture)