## Slide 1: Pipelining I
Prepared by: Noshaba Nasir

## Slide 2: What Is Pipelining?
Pipelining is an implementation technique whereby multiple instructions are overlapped in execution.
It takes advantage of parallelism that exists among the actions needed to execute an instruction.
Today, pipelining is the key implementation technique used to make fast CPUs.

## Slide 3: Real World Analogy
A pipeline is like an assembly line.
In an automobile manufacturing line, there are many steps, each contributing something to the construction of the car.
Each step operates in parallel with the other steps, although on a different car.

## Slide 4: Real World Analogy
Automobile manufacturing line without pipelining, in 3 stages
Assemble (A), Paint (P), Fix tires (T)
Assuming A+P+T take 3 hours
Time line | 0-3 hours | 3-6 Hours | 6 -9Hours
Car 1 | A+P+T |  | 
Car 2 |  | A+P+T | 
Car 3 |  |  | A+P+T

## Slide 5: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
Assemble (A), Paint (P), Fix tires (T)
Assuming each stage takes 1 hour
It takes 5 hours with pipelining and 9hours without pipelining
Speedup = 9/5
Time line | 1st hour | 2nd hour | 3rd hour | 4th hour | 5th hour | 6th hour | 7th hour | 8th hour | 9th hour
Car 1 | A | P | T |  |  |  |  |  | 
Car 2 |  | A | P | T |  |  |  |  | 
Car 3 |  |  | A | P | T |  |  |  | 

## Slide 6: Real World Analogy
Here our assumptions are
  There is no time consumed to transition car from one working station on other
  All the stages consume equal time
However these assumption are not valid
  Each stage can take different amount of time
    For example painting a car takes 2 hours and Assembly and installing types take 0.5 hours each
  To transfer car from one stage to another will take time.
    For example, it takes 10 minutes to transfer a car from Assembly room to paint rooms and 10 minute to transfer from paint room to tire fixing room.
    Note that this will not be consume in un-pipeline factory as everything will be done is same room

## Slide 7: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
If Assemble (A), Paint (P), Fix tires (T) take different time
If Assembly take 0.5 hour, Paint 2 hours and Tires 0.5 hours
  Paint of Car2 cannot start before 2.5th hour because Paint unit is busy with Car1. So after Assembly Car 2 has to wait for 1.5 Hours
  Total time take to complete 3 instructions =7h
Speed Up = 9/7
Time line | 0-0.5h | 0.5-2.5h | 2.5-4.5h | 4.5-6.5 h | 6.5-7 h
Car 1 | A (0.5 h) | P (2h) | T (0.5h) |  | 
Car 2 |  | A (0.5 h) +wait for 1.5 h | P (2h) | T (0.5h) | 
Car 3 |  |  | A (0.5h)+ wait for 1.5 h | P (2h) | T (0.5h)

## Slide 8: Real World Analogy
Automobile manufacturing line with pipelining, in 3 stages
If we add time for transition between stages as well
Total time taken to complete 3 instructions = 7h+40m=7.67h
Speed Up = 9/7.67
Time line | 0-0.5h | Transition time 10 min | 0.5 +10m-2.5h+10m | Transition time 10 min | 2.5h+20m-4.5h+20m | Transition time 10 min | 4.5h+30m-6.5 h+30m | Transition time 10 min | 6.5h+40m -7 h+40m
Car 1 | A (0.5 h) |  | P (2h) |  | T (0.5h) |  |  |  | 
Car 2 |  |  | A (0.5 h) +wait for 1.5 h |  | P (2h) |  | T (0.5h) |  | 
Car 3 |  |  |  |  | A (0.5h)+ wait for 1.5 h |  | P (2h) |  | T (0.5h)

## Slide 9: Real World Analogy::Throughput and Latency
In case of car manufacturing throughput is number of cars create per hour
  From slide 8 throughput with pipelining is 3 Cars/ 7.67 Hours ~0.4 Cars/hour
  From slide 4 throughput without pipelining is 3Cars/9Hours ~ 0.33Cars/hour
  So we can see that the throughput with pipelining is higher.
Latency is time taken to complete one car
  From slide 8 latency with pipelining is 4.5 hours (4.5 hours consumed to create car2 and 3)
  From slide 4 latency without pipelining is 3 hours (3 hours consumed to create each car)
  So we can see that latency is worse with pipelining
Observation: Pipeline does not improve latency, it only improves throughput

## Slide 10: Throughput and latency for n=3
Case | Latency | Throughput | Speed up
Non pipeline | 3 | 3/9=0.33 | NA
Pipeline ideal case | 3 | 3/5=0.6 | 9/5
Pipeline with all stages not of equal time | 4.5 | 3/7=0.42 | 9/7
Non ideal case with latch time | 4.833 | 3/7.67=0.39 | 9/7.67

## Slide 11: Real World Analogy:: Process Cycle
The time required between moving an object one step down the pipeline is a processor cycle
Assume that all stages procced at the same time
  There is only one conveyer belt and it only moves cars to next step when longest stage is complete, i.e. every two hours.*
  Processor cycle will be 2 hours
  Even the car in T stage will be there for 2 hours and will only come out of pipeline when 2 hours of P(of other instruction are completed)
Notes: Its easier if program the conveyer belt in this way. i.e. move ahead every 2 hours as we will be sure that all the stages were complete before preceding.
This will be more clear when we will talk about pipelining in computers.

## Slide 12: Real World Analogy:: Process Cycle
Consider process cycle to be 2 hours, throughput with pipelining is 3 Cars/ 10 Hours ~0.3 Cars/hour
  This is even worse than throughput of un-pipeline
This issue can be resolve if stages are more or less of equal time duration (paint job can be further divided into smaller stages)
Time line | 2hour | 2hours | 2hours | 2hours | 2hours
Car 1 | A | P | T |  | 
Car 2 |  | A | P | T | 
Car 3 |  |  | A | P | T

## Slide 13: Exercise
Divide your paint job in 4 stages, 1st coat, 2nd coat, 3rd coat and drying , each phase takes 0.5 hours.
What will be throughput with these 6 stages for 3 cars?
Ignore the latch/transition time

## Slide 14: Pipeline in Computer:: Frequency
Computer processors can execute one or more instructions per clock cycle, depending on the type of processor.
Frequency of computer is 1/clock cycle
For example if 1 clock cycle= 10 ms;
  Frequency = 1/10ms= 1MHZ
  i.e. 1 000 000 cycles / second
Frequency is AKA as clock speed

## Slide 15: Pipeline in Computer:: Performance
IDEAL CASE
In ideal case i.e. all the stages require same amount of time and ignoring time to transfer data from one stage to another
  Speedup= n*k/ k+(n-1)
  where n is number of instructions and k is number of stages
Time line | T | T | T | T | T
Car 1 | A | P | T |  | 
Car 2 |  | A | P | T | 
Car 3 |  |  | A | P | T
.. |  |  |  | … | ..

## Slide 16: Pipeline in Computer:: Performance Ideal case (Derivations)
If
  All stages take equal amount of time T
  Latch time=0
  Stages =k
  Number of instructions = n
Then
  Clock cycle of pipeline=T, clock cycle of non pipeline= k*T
  Frequency of pipeline=1/T , Frequency of non pipeline=1/k*T
  Time taken to complete n instructions without pipeline= n*k*T= n*clock cycle of non pipeline
  Through put for n instructions without pipeline= n/ n*k*T
  Time taken to complete n instructions with pipeline= (k+n-1)*T= (k+n-1)*(Clock Cycle of pipeline)
  Through put for n instructions with pipeline= n/ (k+n-1)*T
  Speedup for n instructions = n*k*T/ (k+n-1)*T = n*k/ (k+n-1)
  Latency without pipelining = k*T
  Latency with pipelining= k*T

## Slide 17: Pipeline in Computer:: Performance Ideal case
Numerical:
  It takes 6us to complete one instruction in non-pipeline processor
  We were able to convert the circuit into 6 equal sequential pipeline stages.
  Assume latch time is 0
  Answer the following, assuming that there are no stalls in the pipeline.
What are the clock cycle in the two processors?
What are the clock speeds(frequency) in two processors?
How long does it take to finish one instruction in pipeline and no pipeline (latency )?
What is the throughput for 100 instructions without pipelining?
What is the throughput for 100 instructions with pipelining?
What is the speedup from pipelining for 1 instructions?
What is the speedup from pipelining for 100 instructions?

## Slide 18: Pipeline in Computer:: Performance
Another example
  It takes 5us to complete one instruction in non-pipeline processor
  We were able to convert the circuit into 5 equal duration sequential pipeline stages.
  Latch time is 0us
  Answer the following, assuming that there are no stalls in the pipeline.
What are the clock cycle in the two processors?
What are the clock speeds(frequency) in two processors?
How long does it take to finish one instr in pipeline and no pipeline (latency )?
What is the throughput for 100 instructions without pipelining?
What is the throughput for 100 instructions with pipelining?
What is the speedup from pipelining for 1 instructions?
What is the speedup from pipelining for 100 instructions?

## Slide 19: Exercise
Question 1: If throughput of one processor1 for n instruction is 10us and through put of processor 2 is 15us for same n instruction what speed up is achieved by processor2 are compare to processor 1?
Question 2: If Latency with pipelining with 5 stages is 6us and latch time is 0 what is the clock cycle time?